Biological Effects of RF and Microwaves

Camelia Gabriel

Microwave Consultant Ltd. (MCL), Woodford Road, London, E18 2EL

Abstract

The biological effects and the human health considerations of radio and microwave radiation have been the subject of scientific investigations for most of this century.  A great deal of information has been gathered, particularly in the last decades, and much is known about the physics of the interaction between such fields and biological system.  The subject will be reviewed in the light of recent reports in the scientific literature.

The discussion will lead on two subjects: (i) the hypothesis that low-level electromagnetic fields cause biological effects in general and adverse health effects and cancer in particular  and (ii) the suggestion that pulsed fields are more potent than continuous radiation at producing biological effects.

Introduction

The effects of electromagnetic fields on biological systems were first observed and exploited over a century ago.  Concern over the possible health hazards of human exposure to such fields developed much later,  notably in the 1940s, when the use of powerful radar sources during World War II and later, the industrial use of the newly developed magnetron sources, alerted the scientific community to the potential health hazards of the exposure of people to high intensity electromagnetic fields and radiation.  Daily1 (1943) carried out one of the first human exposure studies and H. P. Schwan proposed the first limit on exposure to radiofrequency radiation in 1953 on the basis of physiological considerations, thermal load and heat balance (Schwan and Piersol2 1954).

Current concern over the issue of hazards stems mainly from recent epidemiological studies of exposed populations and also from the results of laboratory experiments in which whole animals are exposed in vivo or tissue and cell cultures exposed in vitro to low levels of irradiation.  The underlying fear is the possibility of a causal relationship between chronic exposure to low field levels and some forms of cancer and the suggestion that pulsed fields are more potent than continuous radiation at producing biological effects.  So far the evidence does not add up to a firm statement on these matter but there is enough uncertainty to create a need for further targeted research (Repacholi3 1998).  At present it is not known how and at what level, if at all, can these exposures be harmful to human health but these are the issues that should be addressed in future research.

This paper will give a brief overview of the current state of research in this field and how it is evaluated  for the purpose of producing scientifically based standards.  The emphasis will be on the physical, biophysical and biological mechanisms implicated in the interaction between em fields and biological systems.  Understanding such mechanisms leads not only to a more accurate evaluation of their health implications but also to their optimal utilisation, under controlled conditions, in biomedical applications.

Mechanisms of Interaction of Em Fields with People

Interactions between em fields and  people occur at all levels of organisation.  The coupling of external fields with the body is the first step leading to further interactions at the cellular and molecular level.  The initial coupling is a function of numerous parameters including field characteristics as well as the size and shape of the body and its electrical properties.  The coupling is most efficient when the size of the body is of the same order of magnitude as the wavelength of the field and when the long axis of the body is in the direction of the field.  A consequence of the primary interaction is that internal fields are induced inside the body.  The internal fields interact with local fields at the level of the cells, in the extracellular space, within cells  and  across cell membranes (Mcleod4 1992).

Internal electric fields act on bound and free charges in the body tissue causing polarisation, molecular orientation and the establishment of ionic currents.  There is little, if any, direct interaction with a magnetic field, instead, time varying magnetic field generate electric fields with the usual consequences.

The frequency dependence of the dielectrical properties of tissues (relative permittivity  and total conductivity ) indicate the nature and extent of the interaction of the tissue with an electric field.  For most tissues,  the relative permittivity is highly frequency dependent from hertz to gigaherts with values reaching 107 below 100 Hz decreasing to less than 50 above 1 GHz (Gabriel et al5, 6 1996).  This and the corresponding frequency dependence of the conductivity values  are illustrated in Fig. 1 for a high water content tissue.  This typical behaviour indicate that strong direct interactions are likely at low frequencies (high permittivity and low conductivity) while at high frequencies, the interactions are dominated by the high conductivity of tissues making energy absorption from ionic and polarisation currents the main outcome.

Fig. 1: Permittivity and conductivity of ovine spleen tissue at 37˚C presented here as an example of the spectrum of a high water content tissue (experimental data from author’s laboratory).

Biological Effects

Cells and tissues exist in a background of bioelectric fields.  For example, some electrically active cells sustain a transmembrane potential of up to 0.1 V (inside negative), cell communications initiate action potentials which are pulse like signals lasting a few milliseconds.  Currents induced by external fields add to and interfere with these ambient fields.

At frequencies below 1 kHz, induced currents flow mainly through the extracellular fluid, they affect the electrical environment of cells, may cause changes in the transmembrane potential, and, if sufficiently intense,  stimulate electrically excitable cells.  Current densities of the order of 0.1 Am-2  are capable of stimulating nerve and muscle cells (Bernhardt7 1988) while higher currents have more serious consequences, this compares with endogenous current densities of between 1 and 10 mAm-2.  Interactions at or below the threshold for stimulation are not isothermal, energy is absorbed but the resulting thermal load is negligible by comparison to the thermal fluctuation of the body.  The threshold for stimulation increases proportionally with frequency, the energy dissipated by that currents increases at a faster rate.  At about 1 MHz, thermal damage to the cells may occur at current densities below the stimulation threshold.

Interactions resulting in thermal effects are described in terms of the power absorbed per unit body mass or specific absorption rate (SAR), such exposures are referred to as thermal and their biological consequences are described as thermal effects.  Lesser exposures that trigger thermoregulatory responses but no appreciable rise in temperature are sometimes referred to as athermal while even lower intensity exposures that do not invoke thermoregulation are referred to as nonthermal.  Thermal exposures and thermal effects are well defined, but the terms 'athermal' and 'nonthermal' are often confused in the scientific literature and used to describe effects ascribed to low-level, or below thermal exposures. Most thermal effects have been observed at SARs in excess of  about 2 Wkg-1 while reported nonthermal effects involve SARs of less than 0.01 Wkg-1.

The hypothesis of an association between the incidence of cancer and exposure to RF radiation is at the centre of ongoing laboratory and epidemiological studies.  This issue was brought to the forefront of the debate by media reports of brain tumours and the use of cellular phones.

Effects on the central nervous system (CNS) are likely to affect health , some of the landmark studies will be reported.

Thermal effects

People are accustomed to receiving thermal stimulation and, provided that these are not too large, the body can deal with them by invoking thermoregulatory responses. The threshold SAR for the onset of thermally induced biological effects, other than thermal regulation, is about 2-4 Wkg-1. This level of SAR may give rise to a temperature elevation of about 1 or 2 degrees and may cause behavioural changes or result in a reduction of performance of learned tasks in experimental animals.  These effects are consistent with the rise in temperature and are therefore classified as thermal effects. The biological effects associated with this and higher levels of SAR are well documented and have been extensively reviewed (Saunders et al8 1991, Polson and Heynick9 1993) they include modification of the action of drugs, changes in the secretion of hormones, developmental abnormalities as well as transient effects on heat sensitive systems such as spern cells and blood forming tissues.  The database of biological effects is consistent with a strong correlation between the SAR and the severity of the resulting biological effect.  For this reason SAR is widely accepted as a means of defining a dose of radiofrequency (RF) radiation to the body.

Nonthermal effects

The hypothesis that high frequency electric fields exert specific, nonthermal,  action on biological materials has been tested by scientists as early as the 1930s (Bateman10 et al 1937).  Interestingly, this question is not yet satisfactorily resolved despite the early effort and the growing number of papers describing subtle biological responses to specific low intensity fields below the threshold for thermal effects (Saunders et al8 1991, Polson and Heynick9 1993, Adey11, 12 1994, 1996).  Pulsed and CW exposure are implicated with no apparent dose response relationship or indication as to which field parameter is responsible for the effect.

Several non linear interaction mechanisms have been proposed to describe some of the experimental results in terms of signal amplification from resonant or cooperative interactions at the site of the cellular membrane.  None has been experimentally tested  At a more fundamental level, the concept of low level interactions leading to significant biological effects has been challenged on theoretical grounds by Adair13 (1991). His main argument is that low-level fields are likely to be masked by thermally generated electrical noise. The absence of dose response together with the lack of well defined mechanism makes it difficult to plan new experiments and even to repeat old ones in different laboratories under identical exposure conditions.  Nevertheless, attempts should be made to replicate at least some key studies.

The following example illustrate the type of research that needs to be replicated.  Degenerative changes caused by low level microwave irradiation in the retina, iris and corneal endothelium of primates were first reported in 1985 (Kues et al14 1985)  followed by several studies by the same research group over a number of years (Kues et al15 1992).  The effects were observed with continuous irradiation but pulsed microwaves were found to be as effective at lower power levels.  Pre-treatment of the eye with the glaucoma drug timolol maleate further lowered the threshold for damage to an average SAR of 0.26 Wkg-1.  Although the authors did not measure intra ocular temperatures in the animals, the results suggest that a mechanism other than significant heating of the eye is involved.  To date there are no reports of replication or non-replication of these results.

Cancer promotion hypothesis

It is generally accepted that low-level RF fields are unlikely to initiate cancer, but a question remains as to whether it can promote its development directly or by enhancing the action of other known carcinogenic agents.  Numerous animal studies were designed to test the promotion/co-promotion hypothesis, some challenge the issue of initiation of cancer.

A series of studies  on RF induced DNA damage were published by Sarkar et al16 in 1994 and by Lai and Singh17, 18 (1995, 1996).  The latter authors reported an increase in DNA single and double-strand breaks in brain cells of rats exposed to pulsed 2.45 GHz fields at average whole body SAR  of 0.6 and 1.2 Wkg-1 for 2 hours.  Their results could be interpreted either as an increase in the rate of DNA breaking or as an inhibition of the repair processes in the cells.  DNA damage is an initial step in the multi-stage process of carcinogenesis and could also lead to neurodegenerative diseases .  More recently, Lai and Singh19 (1997) reported that the treatment of rats immediately before and after the exposure with free radical scavengers, prevents the occurrence of exposure-induced DNA damage and suggest a free radical related mechanism.  The authors refer to the association between an excess of free radicals in cells and various human diseases.  To put this series of studies in perspective it should be noted that no radiation induced DNA damage was found in similar experiments by another research group (Malyapa et al20 1997).

In the DNA damage experiments, the exposures were low-level but acute.  By contrast, a lifetime animal study by Chou et al21 (1992) illustrates investigations of the effect of chronic exposure to low intensity RF fields. The aim of the study was to investigate the effects of long-term exposure to pulsed microwave radiation. The main feature of the study was the exposure of a large sample of experimental animals (rats) throughout their lifetimes in order to monitor them for effects on general health and longevity. The exposed animals were subjected to 2.45 GHz microwaves, square-wave amplitude modulated at 8 Hz, providing a whole body SAR  of between 0.15 and 0.4 W kg-1  throughout the lifetime of the animal.  The results did not show any statistically  significant effects on general health, longevity, cause of death, and lesions associated with ageing and the incidence of benign tumours.  Some positive results on hormone levels and changes in the immune system were not confirmed in a follow up study (Chou et al22 1992).  A statistically significant increase of primary malignancies in exposed rats compared to controls was reported but tumour incidence was lower than historically expected in both groups and did not affect the life-span of the animals.  Overall, the results indicate that there were no definitive biological effects in rats chronically exposed to RF radiation at 2.45 GHz.  One should add that the effects that were reported need independent verification.

More recent animal studies have been designed to test the cancer hypothesis for exposures specific to mobile communications.  The aim of one such study (Repacholi et al23 1997) was to determine whether long-term exposure to 900 MHz fields, modulated in a manner similar to the cellular communications GSM signal, would increase the incidence of lymphoma in a genetically engineered mouse, predisposed to develop the tumours.  The SARs ranged from 0.008 to 4.2 Wkg-1.  It is important that this study be repeated and, if replicated, it should be redesigned to enable a systematic understanding of the outcome.

Effects on the CNS

Other biological effects with potentially serious health implications include changes in the permeability of certain barrier tissues.  A widely studied phenomenon is the increase in the permeability of the neural tissue layer commonly known as the blood-brain-barrier (BBB).  Several authors using high and low levels of RF exposures have shown field-induced increase in BBB permeability, others have not replicated the results.  Salford et al24 (1994) used exposure conditions relevant to cellular communication and reported increased permeability at all levels of exposures down to 0.016 Wkg-1.  These results need replication.

Implications for Standards and Conclusions

Ideally, human exposure standards should be based on rigorous scientific evidence that a physical agent is capable of causing harm under identifiable conditions.  The scientific base underpinning em exposure standards is well established with respect to acute effects, but the issue is clouded by uncertainties provided by the growing database of low levels effects and the suggestion that pulsed fields are more effective initiator of biological effects.  It should be noted that exposure standards are formulated to guard against thermal effects.  Low-level, nonthermal exposures that result in SAR below the level of thermal significance are implicitly assumed safe.

It is important that such studies be continued and that their health implications, if any, be determined before their incorporation into standards.  Future research should be specific in nature, aiming at refining our knowledge of specific effects arising from exposures to electromagnetic fields and radiation.  The relevance of the various field parameters in the interaction with biological material should be investigated such that the effect of pulsing could be clarified.

Because of the difficulties of extrapolating from animal experiment to human reactions, epidemiological studies are needed to underpin our knowledge of health effects and our estimation of risk.  The outcome of future epidemiological studies should guide the direction of laboratory studies.

References

- Daily, L. (1943), A clinical study of the results of exposure of laboratory personnel to radar and high frequency radio, US Nav Med Bull 41: 1052

- Schwan, H.P. and G. M. Piersol (1954) The absorption of electromagnetic energy in body tissues: A review and critical analysis, Am J Phys Med 33: 370-404.

- Repacholi, M. H. (1998) Low-level exposure to radiofrequency electromagnetic fields: Health effects and research needs, Bioelectromagnetics 19: 1-19

- Mcleod, K.J. (1992) Microelectrode measurements of low frequency electric field effects in cells and tissues, Bioelectromagnetics, Supplement 1:1-10, 161-178

- Gabriel, C., Gabriel, S. and Corthout, E., 1996a, The Dielectric Properties of Biological Tissues: 1. Literature Survey, Phys. Med. Biol. 41 (11), 2231-2250.

- Gabriel, S., Lau, R. W. and Gabriel, C., 1996b, The Dielectric Properties of Biological Tissues: 2. Measurement in the frequency range 10 Hz to 20 GHz, Phys. Med. Biol. 41 (11), 2251-2269.

- Bernhardt, H. (1988) The establishment of frequency dependent limits for electric and magnetic fields and evaluation of indirect effects. Radiat. Environ. Biophys. 27, 1-27

- Saunders, R. D., C.I. Kowalczuk and Z. j. Siekiewcz, (1991) Biological effects of exposure to non-ionising fields and radiation: III Radiofrequency and microwave radiation NRPB-R240 (London HMSO)

- Polson and L.N. Heynick, Overview of the radiofrequency radiation bioeffects database, in Radiofrequency Radiation Standards, B. J. Klauenberg, M. Grandolfo and D. N. Erwin (Editors), NATO ASI Series, Plenum Press 337- 388 (1993).

- Bateman, J. B., H. Loewenthal and H. Rosenberg (1937), Alleged specific effects of high-frequency fields on biological substances: Nature: 140: 1063-1064.

- Adey, W. R. (1994) A growing scientific consensus on the cell & molecular biology mediating interactions with environmental em fields.  BICS International Forum on Electromagnetic Transmissions: London

- Adey, W. R. (1996) Bioeffects of mobile communications fields in Mobile Communications Safety: edited by : N. Kuster, Q. Balzano and J.C. Lin  Chapman & Hall

- Adair, R. K. (1991) Constrains on biological effects of weak ELF electromagnetic fields, Physical ReviewA: 43 (2), 1039-1048

- Kues, H. A., L.W. Hirst, G. A. Lutty S. A. D’Anna and G. R. Dunkelberger (1985), Effects of 2.45 GHz microwaves on primate corneal endothelium: Bioelectromagnetics 6:2, 177-188

- Kues H. A., J. C. Monohan, S. A. D’Anna D.S.Mcleod, G. A. Lutty and S. Koslov, (1992)  Increased sensitivity of the non-human primate eye to microwave radiation following ophthalmic drug pretreatement. Bioelectromagnetics 13:5, 379-393.

- Sarkar S., Ali S. and Behari J., (1994) Effect of low power microwave on the mouse genome: a direct DNA analysis., Mutat Res: 320: 141-147.

- Lai H. and Singh N.P., 1995, Acute low-intensity microwave exposure increases DNA single-strand breaks in rats brain cells., Bioelectromagnetics: 16: 207-210.

- Lai H. and Singh N.P., 1996, Single- and double-strand DNA breaks in ray brain cells after acute exposure to radiofrequency electromagnetic radiation., Int J Radiat Biol., 69, 513-521.

- Lai H. and Singh N.P., 1997, Melatonin and a spin-trap compound block radiofrequency electromagnetic radiation-induced DNA strand breaks in rat brain cells., Bioelectromagnetics: 18: 446-454

- Malyapa R.S., E.W. Ahern, W.L. Straube, E.G. Moros, W.F. Pickard and J.L. Roti Roti, 1997,  Measurement of DNA damage by the alkaline comet assay in rat brain cells after in vivo exposure to 2450 MHz electromagnetic radiation., E-2 in Second World Congress for Electricity and Magnetism in Biology and Medicine, Bologna, Italy.

- Chou, C. -K., Guy, A. W., Kunz, L. L., Johnson, R. B., Crowley, J. J. and Krupp, J. H., (1992) Long-term, Low-level microwave irradiation of rats. Bioelectromagnetics. 13. 469-96.

- Chou, C.-K., Clagett, J. A., Kunz, L. L. and Guy, A. W., (1992) Long-term, radiofrequency radiation on immunologocal competence and metabolism, USAFSAM-TR-85-105, MAY, Brooks AFB, TX 78235.

- Repacholi M.H., Bosten A., Gebski V., Noonan D., Finnie J. and Harris A.W., 1997, Lynphomas in Em-Pim1 Transgenic Mice Exposed to pulsed 900 MHz Electromagnetic Fields., Radiation Research, 147, 631-640.

- Salford L.S., Brun A., Sturesson K., Eberhardt J.L. and Prersson B.R.R., 1994, Permeability of the blood-brain barrier induced by 915 Mhz electromagnetic radiation, continuous wave and modu;ated at 8, 50, and 200 Hz. Microscopy Res Tech, 27, 535-542